## Slide 1
SMART HOME AUTOMATION SYSTEM
IoT-Based Home Safety & Automation using ESP8266
PRESENTED BY
Name
ID No.
Mostafa Monoar
20234103379
Mubashsher Salek
20234103371
Rahmatul Munim
20234103386
Mehedi Hassan
20234103384
Md. Jewel Rana
20234103363

## Slide 2
Introduction
Home automation connects everyday household devices to the internet, allowing them to be sensed and controlled remotely.
This project uses an ESP32 microcontroller to monitor fire, humidity, temperature, and motion, and to control a light and a water pump.
All data and controls are available through a simple web dashboard, accessible from anywhere.

## Slide 3
Problem Statement
Traditional homes rely on manual switches — lights and pumps must be operated in person.
Fires can spread quickly, and without early detection, damage and risk to life increase sharply.
Homeowners have no way to check temperature, humidity, or activity outside while they are away.
There is a need for an affordable system that senses, alerts, and can be controlled remotely.

## Slide 4
Objectives
Detect fire early
Sense flame and trigger an instant buzzer alarm
Control appliances remotely
Turn the light and water pump on/off from the website
Monitor the environment
Track real-time temperature and humidity
Sense outside activity
Detect motion and show it live on the dashboard

## Slide 5
Hardware Components
Sensors & Inputs
Flame Sensor
Detects fire by sensing infrared light from flames
PIR Sensor
Detects motion of people outside the house
Humidity Sensor (DHT11)
Reads room temperature and humidity
2 Push Switches
Manual override to control light and pump locally

## Slide 6
Hardware Components
Controller, Actuators & Power
ESP8266 Board
2 Relay Modules
Water Pump
LED (6V)
Buzzer
9V Battery

## Slide 7
System Architecture
Sensors
Flame, PIR, DHT11, switches
ESP8266
Reads sensors, controls relays
Cloud Database
Firebase real-time sync
Web Dashboard
View data & send commands

## Slide 8
Working Principle
Fire safety flow
1
Flame sensor detects fire
Sensor picks up infrared light from flames nearby
2
ESP8266 reads the signal
Microcontroller checks the sensor value continuously
3
Buzzer alarm activates
A loud buzzer sounds immediately at the location
4
Alert shown on website
Fire status updates on the dashboard in real time

## Slide 9
Working Principle
Remote control flow
1
User taps a button
On the website, e.g. turn the light or pump on
2
Command sent to cloud
The request updates a value in Firebase
3
ESP8266 reads the update
The board checks the cloud database continuously
4
Relay switches the device
Light or pump turns on or off as requested

## Slide 10
Website Dashboard
Live temperature and humidity readings, updated automatically
Fire alert banner appears instantly when flame is detected
Motion status shows whether someone is currently outside
ON/OFF buttons for the light and water pump, usable from any device

## Slide 11
Key Features
Fire Detection & Alarm
Flame sensor triggers the buzzer instantly when fire is detected
Remote Light Control
Turn the room light on or off from the website
Water Pump Control
Start or stop the water pump remotely, anytime
Humidity & Temperature Monitoring
Live readings displayed on the dashboard
Outdoor Motion Detection
PIR sensor alerts when someone is detected outside

## Slide 12
Advantages
Improved Safety
Early fire alerts can prevent major damage
Remote Convenience
Control appliances from any device, anywhere
Real-Time Monitoring
Always up-to-date temperature & humidity data
Low-Cost Solution
Built with affordable, easily available components

## Slide 13
Future Scope
Dedicated mobile app for Android and iOS
Voice control using Google Assistant or Alexa
Solar-powered backup for uninterrupted operation
AI-based prediction to detect fire risk before it happens

## Slide 14
Conclusion
This project shows that a few affordable components can build a smart home system that genuinely improves safety and convenience. By combining fire detection, environment monitoring, motion sensing, and remote appliance control into one dashboard, we created a practical, low-cost solution. It also gave our team hands-on experience with IoT, embedded systems, and real-time web control.

## Slide 15
Thank You